## Slide 1: WriteHear
Jesse Miller
Dayton, OH
ISSI

## Slide 2: Overview
What is WriteHear?
  Concept
  How it works
    Software
    Hardware
Testing and analysis
  Hardware
  Software

## Slide 3: What is WriteHear?

## Slide 4: Concept
Audio Voice Recognition
Visual Handwriting Recognition
Audio Handwriting Recognition

## Slide 5: Concept
Sounds produced by handwriting
Recorded by microphone
Transcribed by software

## Slide 6: Motivation
Using audio alone:
Transcribe handwriting
Verify signatures
Send encrypted messages

## Slide 7: Past Research
Sketch Recognition Lab at Texas A&M
Did Not
Did
Continuous character recognition
Noise reduction
Test various sets of characters
Test different hardware setups
Signature verification
Distinguish between uppercase characters with %86.8 accuracy

## Slide 8: Software
Templates
Moving Average
Input Character Signal
Endpoint Noise Removal
Dynamic Time Warping
Result
System Architecture
A
B
C
…
Is Character?
yes
No

## Slide 9: Software
Moving Average
Window Size=45ms
Increment=15ms
Input Signal
Moving Average

## Slide 10: Software
Endpoint Noise Removal
T is a fixed threshold
Moving Average
Noise Removal

## Slide 11: Software
Dynamic Time Warping
Method for Comparison:
Stretches signal along time axis
Independent of signal length

## Slide 12: Software
Sakoe-Chiba band width of 8% used to restrict warping and maximize accuracy
Square root of the signals are used for comparison to maximize accuracy
Dynamic Time Warping
bandwidth
*see appendix for details

## Slide 13: Software
Spellcheck database contains over 58,000 words

## Slide 14: Hardware
Contact Microphone
Thin Writing Surface (2.5x2.5x1/8)”
Acoustically Isolating Base
(1/4” thick)

## Slide 15: Testing and Analysis

## Slide 16: Type of Mic.
Dynamic
Contact
Vs.
Electromagnetic induction
Senses vibrations through air and solid objects
Susceptible to noise
Piezoelectric
Senses vibrations through solid objects only
Significantly less effected by noise
90 dB Noise Test
90 dB Noise Test

## Slide 17: Distance From Mic.
1 inch
48 inches
Vs.
Amplitude = 0.01-0.03
Unaffected by distance
Amplitude = 0.01-0.03
Unaffected by distance

## Slide 18: Surface Size
15 in2
720 in2
Vs.
Time to decay to noise level = 300ms
Less distinct features in writing
Lower amplitude
More susceptible to noise
Tap Test
Tap Test
Time to decay to noise level = 15ms
More distinct features in writing
Higher amplitude
Less susceptible to noise

## Slide 19: Surface Material
Plastic
Metal
Vs.
Negligible effect on amplitude
Negligible effect on amplitude

## Slide 20: Surface Thickness
1/8” Thick
1/2” Thick
Vs.
Amplitude = 0.005-0.01 (1/8th the amplitude)
Amplitude = 0.04-0.05

## Slide 21: Writing Utensil
Pen
Pencil
Vs.
Amplitude = 0.04-0.05
Amplitude = 0.04-0.05

## Slide 22: Accuracy
A-Z | a-z | 0-9 | Spellcheck (A-Z) | Signature
87.5% Based on: 8 Individuals 832 samples | 77.9% Based on: 2 Individuals 208 samples | 91.7% Based on: 3 Individuals 120 samples | 85.9% Based on: 3 Individuals 78 words | Type I Error: 4.8% Type II Error: 6.3% Based on: 3 Individuals 53 samples
Similar sound profiles for different characters lowers accuracy
Character accuracy calculated with a template database of 3 samples per character. A similar method was used by SRL at Texas A&M

## Slide 23: Conclusions
WriteHear is a robust and versatile software that can learn and understand different people’s handwriting
A Contact microphone setup greatly reduces background noise allowing WriteHear to work fine with 90dB (loud traffic)
WriteHear works with various materials and writing utensils
WriteHear can catch a forged signature with over 93% accuracy
WriteHear recognized the upper case letters (A-Z) with 87.5% accuracy, matching the 86.8% accuracy achieved by the Sketch Recognition Lab at Texas A&M

## Slide 24: Future Work
Continue to improve and optimize software
Test more conditions such as how a persons handwriting varies over time
Create a user independent system
Create a more fluid system where the user can write naturally without having to pause between characters

## Slide 25: References
Li, W., & Hammond, T. A. (2011, April). Recognizing Text Through Sound Alone. In AAAI.